|  | ......................... pcs. .............................. € .............................. € GEZE Slimline fanlight opener OL 90 N Activation via spring hinge reverser with crank rod For daily aeration and ventilation on vertically installed top-hung or bottom-hung casements, outward opening. Installation can be carried out from the front, without visible attachment screws. Casement is fitted with safety catch and locking device in the scissors. Casement closing pressure must be adjusted at the casement bracket. Clearance-free activation via spring hinge reverser. For window cleaning, the scissors can be disengaged quickly by pressing the release catch. Rod must be covered using an aluminium profile. Technical data: Opening width: 170mm ( ) with corner operating gear Fz-90, left ( ) with corner operating gear Fz-90, right ( ) with gear Fz-91, for vertical installation ( ) with fixed crank rod ( ) with detachable crank rod ( ) without locking mechanism Leaf width: ........ mm ( ) 1 scissors for casement widths from 400 - 1200 mm1) ( ) 2 scissors for casement widths from 1201 - 2400 mm1) ( ) 3 scissors for casement widths from 2401 - 3600 mm1) 1) Heed panel widths Clear overall width: ........ mm (min. 370 mm) ( ) Soffit depth 0-30 mm ( ) Soffit depth 31-60 mm ( ) With locking mechanism, burglary resistant in accordance with SKG only for soffit depth 31-60 mm Leaf width: ........ mm ( ) 1 locking mechanism, 1 scissors for casement widths from 600 - 1000 mm1) ( ) 2 locking mechanisms 1 scissors for casement widths from 1001 - 1200 mm1) ( ) 2 locking mechanisms 2 scissors for casement widths from 1201 - 1500 mm1) ( ) 3 locking mechanisms 2 scissors for casement widths from 1501 – 2400 mm1) Centre of rod to end Crank rod extended: ........ mm (to be completed by the bidder) Colour: ( ) silver-coloured EV1 ( ) white, 9016 ( ) RAL shade according to choice |
| --- | --- |